## Slide 1
Ministry of Electronics
and Information Technology Government of India
Pranay Shahare
HPC-Tech Department CDAC, Pune
GPU Architecture
One Vision. One Goal... Advanced Computing for Human Advancement…

## Slide 2: Topics
Evolution of HPC
CPU vs GPU
GPU Architecture
CUDA Programming
Flow of a CUDA program

## Slide 3: Evolution of HPC System
Memory
CPU
Sequential program Mega Flops
Shared Memory Giga Flops
Parallel programs using OpenMP and MPI
Multiple nodes Tera Flops
Infiniband (200Gbps) Distributed memory
Memory
CPU
CPU
CPU
CPU
Memory
Memory
…….
NETWORK

## Slide 4: Evolution of HPC System (contd…)
Architecture innovations
Width: 8 bit to 16 bit to 64 bit
Multicore: single processor to multi cores
Instructions per cycle: 4-10 cycles per instructions to 4+ instructions per cycle
Clock rate : 3MHz to 4GHz

## Slide 5: CPU vs GPU : Silicon Budget
 | CPU | GPU
ALU | Less | More
Control | More | Less
Cache | More | Less

## Slide 6: CPU vs GPU : Silicon Budget

## Slide 7: CPU vs GPU
CPU | GPU
Small number of large cores | Large number of small cores
Low latency | High throughput
Optimized for serial processing | Optimized for parallel processing
Designed for running complex programs | Designed for repetitive and complex calculations
Cost efficient for smaller workloads | Cost efficient for bigger workloads

## Slide 8: CUDA
CUDA : Compute Unified Device Architecture
Run programs by utilizing power of GPUs
Extension of C/C++ that allows CPUs and GPUs to work together

## Slide 9: GPU Architecture

## Slide 10: Streaming Multiprocessors
Core
LD/ST - Load and store units
SFU - Special Function units
Warp Scheduler

## Slide 11: GPU Programming Paradigm

## Slide 12: Elements of CUDA program
global void cuda_hello(){
printf("Hello World from GPU!\n");
}
int main() { cuda_hello<<<,1>>>(); return 0;
}
Host code - code that runs on CPU
Device code - code that runs on GPU

## Slide 13: Organization of threads

## Slide 14: Organization of threads (contd…)
Threads
- Kernel executes as a set of threads
Blocks
- Threads are grouped into blocks
Grids
- Blocks are grouped into grids
Kernel executes as a Grid of Blocks of Threads

## Slide 15: Software abstraction

## Slide 16: Dimensions of Grids and Blocks

## Slide 18: Kernel Launch Syntax
// Launch kernel
KernelName <<< grid_size, block_size >>> (...)

## Slide 19: Kernel Launch Syntax
// Launch kernel
KernelName <<< grid_size, block_size >>> (...) KernelName <<< no_of_blocks, threads_per_block >>> (...)

## Slide 20: Kernel Launch Syntax
// dim3 variable
dim3 grid_size (x, y, z) dim3 block_size (x, y, z)
// Launch kernel
global KernelName <<< grid_size, block_size >>> (...)
global KernelName <<< no_of_blocks, threads_per_block >>> (...)

## Slide 21: Kernel Launch
// dim3 variable
dim3 grid_size (3, 2)
dim3 block_size (4, 3)
// Launch kernel
global KernelName <<< grid_size, block_size >>> (...)

## Slide 22: Function qualifiers
 | Executed on | Only callable from
 | device | device
global | device | host
 | host | host

## Slide 23: Function qualifiers
 | Executed on | Only callable from
device | device | device
global | device | host
host | host | host

## Slide 24: 1 Block - threads in 1D
int main()
{
fun <<< 1, 10 >>> ();
}
global void fun()
{
int tx = threadIdx.x; printf(“%d”, tx);
}
0 1 2 3 4 5 6 7 8 9

## Slide 25: 1 Block - threads in 2D
int main()
{
dim3 threadsPerBlock(5, 2);
fun <<< 1, threadsPerBlock >>> ();
}
global void fun()
{
int tx = threadIdx.x;
int ty = threadIdx.y; printf(“%d %d”, tx, ty);
}
0 1 2 3 4
0
1

## Slide 26: Blocks in 1D -threads in 1D

## Slide 27: Blocks in 1D -threads in 1D

## Slide 28: Flow of a CUDA program
Allocate host memory and initialize data
Allocate device memory
Transfer data from host to device memory
Execute kernels
Transfer data from device to host
Reclaim memory

## Slide 29: Flow of a CUDA program
Host code
- Sequential code
int main(void){
// sequential code
}
Host

## Slide 30: Flow of a CUDA program
Host code
- Sequential code
Allocate memory on device
int main(void){
// sequential code
// Allocate memory on device cudaMalloc(...)
}
Host

## Slide 31: Flow of a CUDA program
Host code
- Sequential code
Allocate memory on device
Copy data from host to device
- Copy data from CPU to GPU
int main(void){
// sequential code
// Allocate memory on device cudaMalloc(...)
// Copy data from host to device cudaMemcpy(...)
}
Host

## Slide 32: Flow of a CUDA program
Host code
- Sequential code
Allocate memory on device
Copy data from host to device
- Copy data from CPU to GPU
Launch kernel
- Execute threads in parallel on GPU
int main(void){
// sequential code
// Allocate memory on device cudaMalloc(...)
// Copy data from host to device cudaMemcpy(...)
// Launch kernel KernelName <<< grid_size, block_size >>> (...)
}
Host

## Slide 33: Flow of a CUDA program
Host code
- Sequential code
Allocate memory on device
Copy data from host to device
- Copy data from CPU to GPU
Launch kernel
- Execute threads in parallel on GPU
Copy data from device to host
int main(void){
// sequential code
// Allocate memory on device cudaMalloc(...)
// Copy data from host to device cudaMemcpy(...)
// Launch kernel KernelName <<< grid_size, block_size >>> (...)
// Copy data from device to host cudaMemcpy(...)
//sequential code return 0;
}
Host
Host

## Slide 34: Allocating device memory
In C:
- malloc(...)
- free(...)
In CUDA:
cudaMalloc(Location, Size)
cudaFree()
Location: Memory location on device to allocate memory
Size: number of bytes to allocate

## Slide 35: Copy data from host to device
cudaMemcpy( destination, source, numBytes, direction)
Direction
Host to device (cudamemcpyhtod)
Device to host (cudamemcpydtoh)
Device to device (cudamemcpydtod)

## Slide 36: Running a cuda program
- Save file with .cu extension
- test.cu
Load cuda compiler
  Spack load nvhpc
Compiler the program
  nvcc test.cu -o test
Run the executable
  ./test

## Slide 37: THANK YOU